## Slide 1
Network Engineering Project
Fundamentals of Information Technology
By James CAO
Mar. 2017

## Slide 2
No | Contents | Hours
1 | Project 1 : Switch configuration | 
 | Project 1.1: Basic configuration | 2
 | Project 1.2: VALN configuration | 2
2 | Project 2 : Router configuration | 
 | Project 2.1: Static route configuration | 2
 | Project 2.2: Dynamic route configuration | 2
3 | Project 3 : Firewall configuration | 
 | Project 3.1:Basic configuration | 2
 | Project 3.2:Security rule configuration | 2
Network engineering project schedule

## Slide 3
Project 3 : Firewall configuration
Notes: within

## Slide 4
Upon completion of this project, you will be able to:
Understand the concepts about firewall .
Know how to connect and install the firewall devices.
Know how to configure the firewall.
Project Objectives:

## Slide 5
Contents:
1. Connecting to firewall
2. Basic configuration
3. Security policy configuration
  —Packet filter configuration
  —NAT configuration

## Slide 6
Project Design:
AR12-20 * 3
Team 1
network cable
HUAWEI Switch * 4
AR12-20 * 3
Team 2
network cable
HUAWEI Switch * 4
AR12-20 * 3
Team 3
network cable
HUAWEI Switch * 4
AR12-20 * 3
Team 4
network cable
HUAWEI Switch * 4
USG6300
USG6300
USG6300
USG6300

## Slide 7
1. Connecting to firewall
2. Basic configuration
3. Policy configuration
  —Packet filter configuration
  —NAT configuration
Contents:

## Slide 8
Project 3.1: Basic configuration of Firewall
8 *
1 GE RJ45
2 *
10 GE SFP+
4 *
1 GE RJ45
USG6300
Firewall
LOGO
1 console
port
1 MGM port

## Slide 9
Switch A
GE1/0/5~GE1/0/6
GE1/0/1~
GE1/0/4
PC1 PC2 PC3 PC4
PC5 PC6
VLAN 10
192.168.10.0/24
VLAN 30
192.168.30.254/24
VLAN 20
192.168.20.0/24
LAN A
GE
1/0/24
In the following networking diagram, LAN A connects to Internet through GE1/0/24 of switch A and GE 1/0/0 of firewall.
router 1
PC8
GE 0/0/7
192.168.40.254/24
GE 0/0/0
202.100.100.254
192.168.40.0/24
Firewall(USG6300)
GE 1/0/5
202.100.100.1
GE 1/0/1
192.168.50.1
GE 1/0/0
192.168.30.1
DMZ
Project 3.1: Basic configuration of Firewall
PC7
Internet

## Slide 10
Project Goals:
1. All computers in LAN A (include sub-network VLAN 10,VLAN 20) can access PC7（in DMZ）
2. All computers in LAN A (include sub-network VLAN 10,VLAN 20) can access PC8（in Internet）
PC 8 can access PC7 WEB service（in DMZ）
PC 8 can not access LAN A
Project 3.1: Basic configuration of Firewall
DMZ
LAN
Internet
FW
Deny
Allow
Allow

## Slide 11
1. To connect and access the firewall with web browser:
To connect the PC1 to MGM port at firewall USG6300, and then configure the IP address of PC1 as 192.168.0.100
Access the firewall with the web browser:
https://192.168.0.1:8443
Notice: The default IP address of MGM port is 192.168.0.1,
So if the PC1 need communicate to firewall thought MGM, the IP address must be 192.168.0.2~254
Project 3.1: Basic configuration of Firewall

## Slide 12
The default user name and password is :
UserName: admin
Password: Admin@123
Project 3.1: Basic configuration of Firewall
Notes: The new password: nudt+gfkd2008

## Slide 13
The main UI (default at the dashboard menu)
Project 3.1: Basic configuration of Firewall

## Slide 14
2. To configure the network parameter for the firewall:
Project 3.1: Basic configuration of Firewall

## Slide 15
To modify the parameters for Internet interface :
Project 3.1: Basic configuration of Firewall

## Slide 16
To modify the parameters for DMZ interface :
Project 3.1: Basic configuration of Firewall

## Slide 17
To modify the parameters for LAN interface :
Project 3.1: Basic configuration of Firewall

## Slide 18
The interface list :
Project 3.1: Basic configuration of Firewall

## Slide 19
Switch A
GE1/0/5~GE1/0/6
GE1/0/1~
GE1/0/4
PC1 PC2 PC3 PC4
PC5 PC6
VLAN 10
192.168.10.0/24
VLAN 30
192.168.30.254/24
VLAN 20
192.168.20.0/24
LAN A
GE
1/0/24
In the following networking diagram, LAN A connects to Internet through GE1/0/24 of switch A and GE 1/0/0 of firewall.
router 1
PC8
GE 0/0/7
192.168.40.254/24
GE 0/0/0
202.100.100.254
192.168.40.0/24
Firewall(USG6300)
GE 1/0/5
202.100.100.1
GE 1/0/1
192.168.50.1
GE 1/0/0
192.168.30.1
DMZ
Project 3.1: Basic configuration of Firewall
PC7
Internet

## Slide 20
Default
network
Route
To Internet
3. To configure the route policy for the firewall:
To add default route for the firewall to Wide Area Network(WAN):
Project 3.1: Basic configuration of Firewall

## Slide 21
To add static route for the firewall to Local Area Network( VLAN 10):
Project 3.1: Basic configuration of Firewall

## Slide 22
To add static route for the firewall to Local Area Network( VLAN 20):
Project 3.1: Basic configuration of Firewall

## Slide 23
The static route list for the firewall to Local Area Network:
192.168.30.254
192.168.30.254
Project 3.1: Basic configuration of Firewall
Route
To VLAN 10,20

## Slide 24
Project 3.2: Policy configuration of firewall
4. To configure the Packet Filter policy
To configure the Packet Filter policy for LAN to WAN:
From LAN
Action
To Internet
HTTP
Protocol
Users

## Slide 25
To configure the Packet Filter policy for LAN to DMZ:
From LAN
Action
To DMZ
ICMP
Protocol
Project 3.2: Policy configuration of firewall

## Slide 26
The Packet Filter policy list:
Project 3.2: Policy configuration of firewall

## Slide 27
4. To configure the NAT Policy
To configure the NAT Address pool
Project 3.2: Policy configuration of firewall

## Slide 28
To configure the source NAT Policy for VLAN 10
From VLAN10
To Internet
The source IP will be translate to
202.100.100.1
Project 3.2: Policy configuration of firewall

## Slide 29
To configure the source NAT Policy for VLAN 10
From VLAN 20
To WAN
The source IP will be translate to
202.100.100.1
Project 3.2: Policy configuration of firewall

## Slide 30
The source NAT Policy list:
Project 3.2: Policy configuration of firewall

## Slide 31
4. To configure the service mapping Policy
To configure the service mapping for server 192.168.30.100
Well know
server IP
LAN server IP
Well know
service port
Private
service port
Project 3.2: Policy configuration of firewall

## Slide 32
The service mapping list:
Project 3.2: Policy configuration of firewall

## Slide 33
Project 3.3: Static route configuration(In layer 3 switch)
Switch A
(HUAWEI CE58-55)
GE1/0/1~
GE1/0/4
PC1 PC2 PC3 PC4
Step1: Enter system-view:
<HUAWEI> system-view
Step2: Create VLAN 10:
[HUAWEI] vlan 10
Step3: Assign the interfaces GE 1/0/1 ~
GE 1/0/4 to the VLAN 10:
[HUAWEI-vlan10]port GigabitEthernet 1/0/1
[HUAWEI-vlan10]port GigabitEthernet 1/0/2
[HUAWEI-vlan10]port GigabitEthernet 1/0/3
[HUAWEI-vlan10]port GigabitEthernet 1/0/4
[HUAWEI-vlan10]quit
Step4: Assign IP to VLAN 10:
[*HUAWEI]interface vlan 10
[*HUAWEI-Vlanif10] ip address 192.168.10.254 255.255.255.0
[*HUAWEI-Vlanif10]quit
[*HUAWEI]commit
VLAN 10
192.168.10.254 /24

## Slide 34
Project 3.3: Static route configuration(In layer 3 switch)
Step5: Create VLAN 20:
[HUAWEI] vlan 20
Step6: Assign the interfaces GE 1/0/5
GE 1/0/7 to the VLAN 20:
[HUAWEI-vlan20]port GigabitEthernet 1/0/5
[HUAWEI-vlan20]port GigabitEthernet 1/0/6
[HUAWEI-vlan20]quit
Step7: Assign IP to VLAN 20:
[*HUAWEI]interface vlan 20
[*HUAWEI-Vlanif20] ip address 192.168.20.254 255.255.255.0
[*HUAWEI-Vlanif20]quit
[*HUAWEI]commit
VLAN 20
192.168.20.254 /24
Switch A
(HUAWEI CE58-55)
GE1/0/5~
GE1/0/7
PC5 PC6

## Slide 35
Step8: Create VLAN 30:
[HUAWEI] vlan 30
Step9: Assign the interfaces GE 1/0/24 to the VLAN 30:
[HUAWEI-vlan30]port GigabitEthernet 1/0/24
[HUAWEI-vlan30]quit
Step10: Assign IP to VLAN 30:
[*HUAWEI]interface vlan 30
[*HUAWEI-Vlanif30] ip address 192.168.30.254 255.255.255.0
[*HUAWEI-Vlanif30]quit
[*HUAWEI]commit
GE 1/0/24
VLAN 30
192.168.30.254/24
Switch A
(HUAWEI CE58-55)
Project 3.3: Static route configuration(In layer 3 switch)

## Slide 36
Project 3.3: Static route configuration(In layer 3 switch)
[~HUAWEI] display vlan

## Slide 37
Step11: Configure the static route for layer 3 switch:
[~HUAWEI] ip route-static 0.0.0.0 0.0.0.0 192.168.30.1
[~HUAWEI]commit
Step12: Display routing table:
[*HUAWEI]display ip routing-table
Project 3.3: Static route configuration(In layer 3 switch)

## Slide 38
Project 3.3: Static route configuration(In layer 3 switch)
[*HUAWEI]display ip routing-table

## Slide 39
In the Router AR1220E-S:
Step1: Enter system-view:
<Huawei>system-view
Step2: Change the interface link-type to access:
[Huawei]interface GigabitEthernet 0/0/0
[Huawei-GigabitEthernet0/0/0]port link-type access
[Huawei-GigabitEthernet0/0/0]quit
Step3: Create VLAN 60& Assign the interfaces:
[Huawei]vlan 60
[Huawei-vlan30]port GigabitEthernet 0/0/0
[Huawei-vlan30] quit
Step4:Assign IP address to VLAN 60:
[Huawei]interface vlan 60
[Huawei-Vlanif30]ip address 202.100.100.254 255.255.255.0
router 1
(AR1220E-S)
GE 0/0/7
GE 0/0/0
PC8
VLAN 60:202.100.100.254/24
Project 3.3: Static route configuration(In AR1220E-S)

## Slide 40
Step5:Change the interface link-type to access:
[Huawei-GigabitEthernet0/0/7]interface GigabitEthernet 0/0/7
[Huawei-GigabitEthernet0/0/7]port link-type access
Step6: Create VLAN 40:
[Huawei]vlan 40
[Huawei-vlan40]port GigabitEthernet 0/0/7
[Huawei-Vlanif40]quit
Step7:Assign IP address to VLAN 40:
[Huawei-Vlanif40]interface vlan 40
[Huawei-Vlanif40]ip address 192.168.40.254 255.255.255.0
[Huawei-Vlanif40]quit
router 1
(HUAWEI AR1220E-S)
GE 0/0/7
GE 0/0/0
PC8
VLAN 40:
192.168.40.254/24
Project 3.3: Static route configuration(In AR1220E-S)

## Slide 41
Project 3.3: Static route configuration(In AR1220E-S)
[Huawei]dis vlan brief

## Slide 42
Step 10:Verify the communication in PC1,PC2,PC3, PC4 and PC8
ping 192.168.10.1,2,3,4…
ping 192.168.40.1…
Project 3.3: Static route configuration(In AR1220E-S)
Switch A
GE1/0/5~
GE1/0/6
GE1/0/1~
GE1/0/4
PC1 PC2 PC3 PC4
PC5 PC6
VLAN 10
192.168.10.0/24
VLAN 30
192.168.30.254/24
VLAN 20
192.168.20.0/24
LAN A
GE
1/0/24
PC8
GE 0/0/7
192.168.40.254/24
GE 0/0/0
202.100.100.254
Internet
192.168.40.0/24
Firewall(USG6300)
GE 1/0/5
202.100.100.1
GE 1/0/1
192.168.50.1
GE 1/0/0
192.168.30.1
DMZ
PC7

## Slide 43
Project 3.3: Static Routing Configuration(In router)

## Slide 44
Thank You !